## Slide 1: JCSPre: The Robot Edition To Control LEGO NXT Robots
Jon KERRIDGE,
Alex PANAYOTOPOULOS
and
Patrick LISMORE

## Slide 2: Motivation
Can JCSP be implemented on a LEGO NXT?
Why not just use the Transterpreter approach?
Wanted to use Java
  Relates better to previous experience
  More people use Java than occam
  Influence people in the wider community
  Might convince people that the Java thread model can be avoided
  Demonstrate reuse in a fun environment
  Promote plug and play capability
  Eclipse IDE can be used directly

## Slide 3: Questions Posed
Does it fit on a LEGO NXT robot
Which subset of JCSP is required
Which Java environments are available
How many processes can be accommodated
Can we utilise existing JCSP design patterns
Can we exploit further capabilities of the LEGO NXT robot, such as Bluetooth

## Slide 4: Java Environment
Obvious one is LeJOS
  Already contains LEGO NXT abstractions
  Appears to be small
  Already contains a threading model used by JCSP
  Takes account of the processors used in LEGO NXT
  Still being developed
Other JVMs
  IBM J9 and NSIcom CrE-ME
    Designed for embedded CDC market
    Designed for Windows CE
    Not available for LEGO NXT processor combination.
    Fully functional

## Slide 5: Choosing JCSP Package Subset
org.jcsp.lang
  Provides the fundamental CSP capabilities
org.jcsp.util
  Provides channel buffering capability
org.jcsp.awt
  Provides a ‘parallel’ AWT capability
  Not required on LEGO NXT
org.jcsp.net
  Provides the network capability
  Not required (yet) on LEGO NXT

## Slide 6: LeJOS JVM Capabilities
LeJOS JVM is not a full Java implementation
  Limited garbage collection
  Variables of type long cannot be manipulated
  The class Class is not implemented
  The LeJOS API is missing many classes considered fundamental to the core Java API.
  The LeJOS classes are closer to the CLDC Java specification

## Slide 7: Included JCSP Fundamentals
Required system structuring features
  CSProcess,
  Alternative (requires Barrier and Guard),
  Parallel (requires ParThread),
  CSTimer,
  Skip
Communication (Object and int versions of each)
  One2One Channel and One2One ChannelImpl
  ChannelInput and ChannelOutput
  AltingChannelInput
  The Any, Call and Connection versions not included

## Slide 8: LeJOS Abstractions
Sensors (two types)
  A-D sensors (based on previous RCX robot)
  I2C sensors ( newer , more esoteric sensors)
Motors
  Movement (angular and power)
  Tachometer input interface
Communications and Other devices
  Bluetooth
  GPS
  Keyboards
  Interaction with ‘host’ PC (for debugging)

## Slide 9: Sensor Process Architecture
Each sensor type is implemented with a channel interface, hiding the underlying LeJOS abstraction
The associated event listener is contained within the sensor process
Output Channel
Configuration Channel
Sensor

## Slide 10: Motor Process Architecture
Input Channel to set motor speed
Configuration Channel to set operating parameters
  Halting behaviour – Stop or Float
  Speed input – rotational or power based
Termination of all processes is achieved by sending a known value, Integer.MAXINT, to the configuration channel or input channel if available.

## Slide 11: Architectural Framework
LeJOS Java kernel
LeJOS LEGO NXT abstraction for buttons, LCD
display, motor, light ,sound, touch, ultrasound and Gyro and Acceleration I2C sensors
JCSPre
Channel Interfaced Active Components
Application Specific Control and User Interface Processes
LeJOS Firmware

## Slide 12: Active Sensors
Implement the Interfaces
  CSProcess
    Requires a run() method to be executed as part of a Parallel
  SensorPortListener
    Requires a stateChanged() method that is called whenever an A to D type sensor value changes
    I2C sensors do not use this interface and the active sensor process has to periodically read the device ports to determine its current value
A delta value configured into a sensor to ensure that only changes of sensor value greater than delta are written to the sensor’s output channel.

## Slide 13: The JCSPre packages
lang
  Provides the basic JCSP capability
io
  Provides the sensor and motor abstractions
  Provides the Bluetooth receive and transmit processes
plugnplay
  Provides multiplexers, and other processes used to test the system’s operation and which can be used in designs
filters
  Provides threshold filters that can be used in designs
rconsole
  Provides processes that communicate message strings to a PC over usb or bluetooth communication links.

## Slide 14: Threshold Filters
Binary and ternary filters are provided.
  The input value is output on one of the output channels depending on its relationship to threshold values
  Threshold values communicated on the configure channel, or in the process constructor
Binary
configure
above
below
Ternary
configure
above
below
between

## Slide 15: Feasibility Testing (LeJOS)
Underlying LeJOS thread model could spawn 160 child processes from a single parent
A simple variant placed a single integer in each spawned child thread.
  The number of child processes reduced to 90.
The number of threads is dependent on the size of each thread.

## Slide 16: Feasibility Testing (JCSPre)
Parallel
  An integer Producer process, followed by N Add processes that input a number, add a constant to it and then output the new value. The final value is output to the LEGO NXT LCD screen by a final process.
  N = 78 was the maximum number of ‘Add’ processes.
Alternative
  N processes each output to a multiplex process that inputs from each input channel once in each cycle.
  N = 76 was found to be the upper limit

## Slide 17: Feasibility Testing Implications
System does seem capable of supporting sufficient processes provided
  A lot of very small processes are not used
  Especially when ‘hidden’ inside other processes
    Delta and DynamicDelta from ‘standard’ JCSP would be inappropriate
    use the ProcessRead and ProcessWrite capabilities of JCSP

## Slide 18: Bluetooth Communication (NXT)
LEGO NXT robots are provided with Bluetooth capability
Processes in the JCSPre.io package provide Bluetooth Transmit and Receive capability that permit communication between
  LEGO NXT and a PC
  LEGO NXTs
The communication is implemented using the Bluetooth Serial Port Protocol (btspp)

## Slide 19: Bluetooth Communication (PC)
A Bluetooth Connection process has been provided to interact with a JCSP system running on the PC
Uses the ActiveSerialPort concept (CPA- 2004)
Uses a javax.comm implementation appropriate to the platform
  Implemented on PC using Windows XP
  Implemented on PDA using Windows Mobile

## Slide 20: Designing Robot Controllers with JCSPre
The majority of the required processes already exist
  Contained within the JCSPre packages
    lang, io, plugnplay, and rconsole
  ‘Simply’ a matter of connecting them together with channels
Implementer designed control process
Systems can be developed totally within an Eclipse environment
  The code can also be uploaded into the LEGO NXT from within the Eclipse environment.

## Slide 21: User Interface Steerable Robot
PC or PDA based user interface sends motor movement data to robot using Bluetooth.
  Data comprises pairs of speeds for left and right motors
  Only the Distribute Data process was written specially
BTReceive
Left Active Motor
Right Active Motor
Distribute Data

## Slide 22: Steerable Robot
Robot has two light sensors pointing at ground
Robot is steered by sensing either a white or black line across its path.
The sensors align themselves with the line
  If it is white line it just continues
  If it is a black line the robot reverses
Placement of the lines in the path of the robot mean that it can be made to follow a pre-determined route.
The initialisation of the Robot is carried out using an interface on PC connected by Bluetooth

## Slide 23: Steerable Robot Design
BTReceive
Controller
ActiveLightSensor
ActivLightSensor
TriThreshold
TriThreshold
White Grey Black
White Grey Black
Sensor Output
Sensor Output
ActiveMotor
ActiveMotor
configure
configure

## Slide 24: Subsumption Architectures
Brooks Subsumption architecture describes a robot control environment whereby the behaviour of a robot can be broken up into layers of increasing complexity.
Lower levels can have their outputs subsumed by higher levels
This has been achieved in a subsumption package
  This does NOT use the subsumption package available in LeJOS, which is a very partial implementation
  Contains a subsumption pattern that can be modified to specific requirements

## Slide 25: Light Seeking Robot
Light SeekingRobot
  Comprises two cross-coupled Light to Motor (L2M) controllers; due to Braitenburg
Active
Light
Sensor
Black
Hole
Switch
AddN
Scale
Active
Motor
Light Seeking Controller
Active
Light
Sensor
Black
Hole
Switch
AddN
Scale
Active
Motor
L2M
L2M

## Slide 26: Adding Obstacle Avoidance
The Active Motor behaviour has to be subsumed by a higher level behaviour: Obstacle Avoidance
Active
Light
Sensor
Black
Hole
Switch
AddN
Scale
Subsumption
Active
Motor
Light Seeking Controller
Active
Light
Sensor
Black
Hole
Switch
AddN
Scale
Subsumption
Active
Motor
L2SM
L2SM

## Slide 27: Obstacle Avoiding Architecture
Ultrasonic Sensor added to detect obstacles and impose an avoidance behaviour: unequal reversing
Ultrasonc
Sensor
Obstacle
Avoider
Active
Light
Sensor
Subsumption
Active
Motor
Active
Light
Sensor
Subsumption
Active
Motor
L2SM
L2SM
Light Seeking Controller

## Slide 28: Subsumption Design Pattern
The Subsumption Process architecture is provided as a design pattern that has to be specialised to each specific application
Comprising
  Input Sites with an input and several suppressor channels
  Output Sites with an output and several inhibitor channels
  An optional Reset Process with reset channels
  An Inner Process that implements the control aspect

## Slide 29: Input and Output Sites
The number of Input and Output Sites depends upon the application.
Each site holds a single data value
The Inner Process can access the site data value by means of read and write methods.
The Reset Process is able to return the data values in the Input and Output sites to a predefined value, by using the site data value access methods.

## Slide 30: Subsumption Pattern Architecture
Input
Site
Output
Site
Reset
Process
Inner
Process
input
Input
Site
input
output
Output
Site
output
suppressors
inhibitors
resets
read method call
write method call

## Slide 31: Conclusions
An implementation of JCSP on a LEGO NXT has been achieved
Sufficient processes can be utilised to enable the construction of relatively complex control systems
It could (will) provide a vibrant way of teaching Communicating Process Architecture concepts to students
It is fully integrated into the Eclipse IDE
The use of Java makes it more accessible to more people

## Slide 32: Future Work
Produce a publicly available library
Develop the teaching notes
Implement a networking capability based upon Bluetooth so that several robots can communicate through a Bluetooth Server with each other
  Using Kevin Chalmer’s lightweight network protocol
Implement a graphical design tool for the Eclipse environment that allows graphical system design
Determine the limit to control system complexity under more complex operating conditions